## Slide 1: DASH High Availability
Protocol Definition Working Group

## Slide 2: Motivation

## Slide 3: Workgroup Goals
Requirements
E2E flows
  Testing and observability
  Smart Switch
  SLB
  Etc.
Control plane
Data frames
Behavioral model
Combine into formal protocol definition

## Slide 4: Requirements
0 downtime planned failover
<2 sec downtime unplanned failover
Ability to resume connections in event of both unplanned and planned failover (active-standby and active-active scenarios, potentially active-active-active)
All flow table from active device is replicated to others
Link flapping
Asymmetrical flows – SLB
In case of normal operation, flow is forwarded by the same device that learned it
No complicated hashing logic in switches to ensure packets land on right appliance
If appliance receives a valid packet, it must not drop it due to flow replication delays
Ensure both inbound and outbound packets transit the same appliance for a given flow – tradeoffs – either reduce bandwidth or lose some connections
Interoperabililty (in both failover and live migration?)

## Slide 5: Requirements cont.
HA Interoperability is required between vendors
The HA packet format and protocol must be public
The HA protocol for syncing active flows could have a base mode and optional modes
The HA protocol does not need to reliably sync 100% of the flows between cards HA protocol, as a goal, should sync 100% of the flows
Observability to measure successful/failed synchronization

## Slide 6: Requirements cont.
Extendable for future use cases
  E.g. modes of operation
  Extensibility to the messages
Resync a new peer (or previously failed/down device)
  Method of signaling to the network is outside of HA protocol
  State machine signaling only is signaled to the peer
Control over BGP advertising (like bgp-fib-pending) only after resync is done
  Control plane to have visibility into resync status
Config sync by controller, out of scope for the HA protocol

## Slide 7: HA Requirements (short version)
Minimize the possibility of established connections breaking after a failover. [P0]
Minimize link bandwidth HA state synchronization. [P0]
Common control plane API. [P0]
Interoperability between different vendors. [P1]

## Slide 8: Control Plane API

## Slide 9: Topology constraints and assumptions
Peers share the same VIP
Backup peer advertises a longer path for the VIP
Some ENIs are active on one of the peers, and some are backup

## Slide 10: HA Peer Session
IP Address – peer IP address (not a shared VIP)
  Type – IP address
  Mandatory
Administrative state
  Type – enum {down,up}
  Mandatory
Role
  Type – enum {active,backup}
  Mandatory
ENI list – ENI list to be synced with this session (For active role, connections belonging to these ENIs are sent to backup)
  Type – list of ENI
  Mandatory
Operational state
  Type – enum {down,up}
  Read-only
Message batch size – max number of messages to be compressed in one update message
  Type – unsigned int
  Optional
Message batch timeout – the greatest latency allowed before a newly learned connection is sent to a peer if batch is not full
  Type – uSec
  Optional

## Slide 11: Session operational state notification
Session ID – session SAI ID
  Type – SAI object ID
State
  Type - Enum {up, down}

## Slide 12: Statistics
Tx packets/bytes
Rx packets/bytes
Rx packets not received
# of flows currently synced