## Slide 1: DASH Test framework Demo on Intel IPU
Reshma Sudarshan, Volodymyr Mytnyk

## Slide 2: SAI PTF Test Harness for DASH
Auto-generated Python based dataplane testing framework
Thrift wrapper functions to call C-based SAI functions
Generated wrapper functions for SAI which can instead be generated based on SAI headers
DASH related enhancements:
Auto-generation framework and Underlay Test cases adopt to platforms with fewer ports
Auto-generation framework for DASH SAI APIs meta infrastructure
DASH and new Overlay test cases using this new framework

## Slide 3: Demo Scenarios
Vnet to Vnet scenario using SAI thrift API.
  ENCAP + routing outbound traffic flow example.
  DECAP inbound traffic flow example.
Run scenarios using PTF framework.
  Run Vnet inbound and outbound scenarios.
  Stateless underlay ACL (DMAC) for network-to-host traffic.

## Slide 4: SW Components and Traffic Flow

## Slide 5: Inbound traffic flow support scenario
Configure inbound rules on IPU using auto-generated python SAI thrift client APIs.
Send VxLAN packet into network-to-host direction with VNET 2 header using PTF.
Check if packet matches ENI, otherwise dropped.
Check if packet matches outer SIP PA, otherwise dropped
Ensure that the packet matching inbound routing is DECAP.

## Slide 6: Inbound scenario packet details

## Slide 7: Scenario live demo

## Slide 8: Outbound traffic flow support scenario
Configure outbound rules on MEV using auto-generated python SAI thrift client APIs.
Send IP (DECAP) packet to host-to-network direction with VNET 1 address using PTF.
Check if packet has been encapsulated according to CA-PA mapping routing table and correct VNET has been set in the VxLAN header.

## Slide 9: Outbound scenario packet details

## Slide 10: Scenario live demo

## Slide 11: Thank you !